Page 1

brief communications

NATURE | VOL 412 | 5 July 2001 | http://www.nature.com/

page 42/43

F

Figure 1 Insects cause multiple power levels from wind turbin es. a, Example of two power levels at the

same wind speed on different dates. b, The stall flag, consisting of a hinged flap and a reflector. c, Stall

flags, showing the separated flow area on an aerofoil. d, Recording of stall flag signals from the NEG

Micon turbine in California. The light tracks are produced by reflected light from open stall flags. e,

Illustration of the insect hypothesis proposed to explain multiple power levels. f, The two turbines used

for the validation of the insect hypothesis; these were only 50 m apart to ensure equal air inflow. g, The

power curves for the two turbines with 'rough' and 'clean' blades, which are similar to those in a.

d

e

c

f

a

g

flap

sticker

reflector

hinge

airfoil surface

separated flow

attached flow

closed stall flags

open stall flags

airfoil

V[m/s]

P[%]

100

50

0

0 5 10 15 20 25

insects

fly

stagnation

at leading edge

suction peak

at leading edge

rain

do not fly

wind speed [m/s]

Multiple power levels

power [kW]

0

100

200

300

400

500

600

700

4

6

8

10

12

14

16

18

20

22

24

after

July 26

before July 11

0

100

200

300

400

500

600

700

4

6

8

10

12

14

16

18

20

22

24

rough'

clean'

wind speed [m/s]

Power curves of turbines 'rough' and 'clean'

power [kW]

b

Insects can halve

wind-turbine power

or no apparent reason, the power of wind

turbines operating in high winds, may drop,

causing production losses of up to 25%

1

.

Here we use a new flow visualisation technique to

analyse airflow separation over the bl ades and

find that insects caught on the leading edges in

earlier low-wind periods are to blame. These

potentially catastrophic power glitches can be

prevented simply by cleaning the blades.

Unpredictable changes in power levels have

been noted on wind farms in California, with

power sometimes falling to half the output

predicted from the turbine design and generating

two or more different power levels at the same

wind speed (Fig. 1a). Although this phenomenon

(termed 'double' or 'multiple' stalling) has been

investigated

2-4

, the cause has remained unknown.

One study

5

commissioned by a turbine

manufacturer (NEG Micon) used a new invention

called a stall flag

6

(patent, Energy Centre of the

Netherlands) as a flow-separation detector (Fig.

1b) to try and solve the problem. This device

works on the principle of a hinged flap that opens

up in a separated airflow to uncover an individual

reflector (Fig.1c) which allows the flow to be

visualised. Operation of a stall flag on a turbine

with a rotor diameter of 44 metres is illustrated in

Fog. 1d, in which the light tracks are from

exposed reflectors and indicate where the blades

stall.

We found that the stalling behaviour of the

blades depends on the degree of contamination of

the leading edges. However, the red uction in

power should be continuous (as debris on the

blades would be expected to accumulate

gradually) rather than stepped in distinct levels as

shown in Fig. 1a.

We considered the possibility that flying

insects caught on the turbine blades could explain

this effect. Insects prefer to fly in conditions of

high air humidity, low wind and temperatures

above about 10C. Under these conditions, they

will increasingly foul the leading edges of the

blades. In low winds, the incident angle between

the flow and the blades is small, which

corresponds to low air velocity around the leading

edges, so the blade is not susceptible to

contamination of the leading edges and the power

output is unaffected. Insects rarely fly in high

winds, so turbines operating in steady high-wind

conditions do not become contaminated and

power levels remain constant.

In high winds, however, the angle between the

flow and the blades increases and the aerodynamic

suction peak (the area of minimum pressure and

maximum air velocity) shifts to the leading edge.

If this happens to be already spattered with dead

insects, power output will fall: the greater the

contamination at the suction peak, the sooner the

blades will stall and the more lift will be lost (Fig.

1e). Thus after each period of low wind, the

amount of insect contamination may change,

causing a different power level to be produced in

high winds.

We verified this hypothesis experimentally by

using stall flagging to compare airflow over

smooth blades with that over blades that have

been artificially roughened on their leading edges

(by installing a zigzag tape of maximum thickness

of 1.15 mm) The two turbines were within 50

metres of each other to ensure equal inflow (Fig.

1f). A 25 Hz digital video camera recorded

the stall flag signals, providing thousands of

computer-processed images which indicated

that flow separation on the roughened blades

was significantly increased at wind speeds of

11-25 m s

-1

. This effect extended over the

entire blade span, which explains the

previously observed power losses (Fig. 1a).

Moreover, power output from rough - and

smooth -bladed turbines was equal at low

wind speeds, but higher from the 'clean'

blades at high wind speeds (Fig. 1g), neatly

reproducing the effect shown in Fig. 1a.

We also studied a time series for the

power output from four different turbines and

fiound that the power at high wind s peeds

decreased markedly after every period of low

wind speed, rising again after the blades were

cleaned either manually or by rain, as

expected. It is likely that accumulation of ice

or dirt on the blades could create distinct

power levels in high winds in the same ways

as insect contamination.

Gustave P. Corten*, Herman F. Veldkamp

†

*Energy Centre of the Netherlands (ECN), Unit Wind

Energy, P.O. Bo x 1, 1755 ZG Petten, The Netherlands

e-mail: corten@ecn.nl

†

NEG Micon A/S, Alsvej 21, 8900 Randers, Denmark

1. Madsen, H.A., Aerodynamics of a Horizontal Axis Wind

Turbine in Natural Conditions, (Risœ M 2903,

Denmark, 1991).

2. Dyrmose, S.Z., Hansen, P., The Double Stall

Phenomenon and how to Avoid it (IEA Joint Action

Aerodynamics of Wind Turbines, Lyngby, 1998).

3. Snel, H.; Corten, G.P.; Dekker, J.W.M.; Boer, J. de,

Chaviaropoulos, P.K., Voutsinas, S., Progress in the

Joule Project: Multiple Stall Levels , (EUWEC proceed.,

Nice, 1999).

4. Bak, C., Madsen, H.A., Fuglsang, P., Rasmussen, F.,

Wind Energy 2, 195-210 (1999).

5. Corten, G.P., Insects Cause Double Stall, 13

th

IEA

expert meeting on the Aerodynamics of Wind Turbines,

(Stockholm, 1999).

6. Corten, G.P., Flow Separation on Wind Turbine Blades,

Ph.D. thesis, (University Utrecht, Utrecht, 2001).

Page 2

SCIENCE NEWS, Vol. 160 No. 5, p.73, August 4, 20

In California, wind turbine operators have learned from experience that if they regularly wash insect

debris off their turbines, they avoid performance dips. But the pattern of dips defied the obvious

explanations - that dead insects piling on the blades were slowly sapping turbine power, notes Herman F.

Veldkamp of wind-turbine maker NEG Micon of Randers, Denmark. Instead turbine operators found that

their machines' bug-encrusted vanes lost power in steps. Though operating fine in low winds. With each

return of high winds, the step-down woul d be worse. Veldkamp and Gustave P. Corten of the Energy

Center of the Netherlands in Petten have sleuthed out the reason behind this. The duo report its findings in

the July 5 N

ATURE

. ----- P.W.

Corten/Veldkamp, September 2001:

'Our project was initiated by a turbine owner in

California who observed that his turbines could have

distinct levels in the same wind. The owner had

experience with turbines for more than a decade. He

knew for example that spattered insects on the blades

could reduce power significantly. However, he did not

hold insects responsible for the observed distinct

power levels. The argument was that insect-

contamination was expected to build -up progressively

and thus would decrease power gradually, in

contradiction to the observed distinct levels. The

phenomenon became even more elusive since

unsubstantiated reports came in that the power could

suddenly jump from one level to another. Nobody

could imagine how insect-contamination could

suddenly increase or decrease in minutes. The third

argument against the insects was that insect-

contamination was expected to influence power at low

wind too, which was not observed.

In the beginning of the project insect-contamination

was rejected as hypothesis and we formulated 10

other hypothetical explanations. After weeks of flow

visualisation experiments, set up to test these other

hypotheses, most of them were rejected too. We alm ost

had to go home without finding an explanation.

During the last days of our stay in California we were

forced to reconsider all hypotheses including the

insect-contamination. We looked into time series of

power and could not find any jump, bu t we saw that

the power in high wind was lower after each period of

low wind. This was the point where we came with the

model that insects only fly in low wind, thus only then

increase contamination. When the wind speed

subsequently increases, the level of contamination is

constant (insects do not fly in high winds) and this

advances stall and so brings up a new distinct power

level...', see further in N

ATURE

's article.